## Slide 1
Bryce Miller, Alessandra Hruschka, Gina Maliekal
Group 11
User Friendly
Fastening Device
(UF-FD)
Notes: UF-FD for AFO application

## Slide 2: Review of Project

## Slide 3: Design Need
AFOs – promoting proper ambulation
cerebral palsy patients
donning/doffing – introduction of user error
  misalignment of orthotic and foot
  deviation of treatment; exacerbation of deformity
rigid AFO – body, distal strap, proximal strap
proximal strap significant source of user error
  patients and/or caretakers
Notes: a significant application of AFOs – ankle foot orthotics – is correcting foot deformities and strengthening particular muscle groups in the leg and foot
cerebral palsy patients represent a significant portion of the patient population making up the target consumer group for the AFO-FD

## Slide 4: Current Solution
doubled over velcro strap

## Slide 5: Design Requirements
compatible with anthropometric parameters of patient’s leg
  minimum orthotic opening – 3 in.
lightweight
  mass < 35 ounces
ease of donning/doffing
  single-handed use
  minimalistic instruction
product life
  resistance to wear, corrosion, component failure
inconspicuous
  requires actual input from children patients
low maintenance
  no special care required
low cost
  entire AFO <$500
compatible implementation with existing AFO manufacture

## Slide 6: Overview of Chosen Concept
Mechanism Style: Rack and Pinion System
Further Addition: Visual Indicator System for Assessing Tightness
Notes: primary selection was in choosing a particular style; “style” used to refer to different approaches, drawing upon imagination but upon methods of locking and fixing features together, some in strapping applications from other industries and some from entirely unrelated applications

## Slide 7: Analytic Efforts

## Slide 8: Assessment of Tightening Forces
How tight is “tight enough”?
  pertinent to the indicator system
  desired tightening force measure “stored” within springs
initial theoretical approach
  compression of springs (Hooke’s Law) equating to the tension in the straps
  too many unknowns
Normal Force
Strap Tension Forces
α
Notes: evaluating the forces involved two essential considerations, the first was determining “how tight is tight enough?”

## Slide 9: Assessment of Tightening Forces (cont’d)
solution: collection of empirical data and selection of specific spring geometry
spring scale with existing strap design with 21 yr old female subject
  average force from repeated trials was 5.0 lb
    four springs; each to be 1.25 lb
  spring displacement: 0.25 in
  Hooke’s Law
    F = -kx … k = -F/x
    k = 1.25lb /(.25in) = 5 lb/in
Notes: springs in parallel

## Slide 10: Assessment of Loading Forces
What will be peak loading?
45 lb max load – Silva et al
failure point
material deformation strengths
Silva et al.
Notes: failure point expected to be wire rope (75 lb max loading)

## Slide 11: Sizing Considerations
anthropometric data of calf circumference
  minimum two sizes
  data of a 5-yr old; focus on CP patients
  stunted growth and atrophied muscles
  orthotic opening 1/3 of calf circumference
CP (5 years old) Children: Calf Circumference (cm) |  |  |  |  | 
Male |  |  | Female |  | 
10% | 50% | 90% | 10% | 50% | 90%
25.9 | 29.9 | 35.5 | 27 | 30.6 | 36.5
Data from: http://www.cdc.gov/nchs/data/nhsr/nhsr010.pdf |  |  |  |  | 

## Slide 12: Specific Details of Chosen Design

## Slide 13: Design Overview – The Big Picture
1¾”
3”
1 1/3”

## Slide 14: User Interface / Indicator System
Shell, Spring Base, Knob
Tightening forces spring base into shell
Push/pull of knob to lock/unlock
Notes: Safety
  Racks and straps
    metal racks always contained within housing; straps only component passing through shell wall
  components fixed together via screws

## Slide 15: Housing Pieces
Base
Cover Plate

## Slide 16: Housing Pieces (cont’d)
Shell
Indicator Spring Base
Notes: ABS material – high mechanical and tensile strenght, medium pricing, molded/fabricated easily; electrically insulated
Delrin for prototyping

## Slide 17: Gear Mechanism

## Slide 18: Gear Mechanism & Tightening
Notes: Moving into the House

## Slide 19: Locking the Gears

## Slide 20: Locking the Gears (cont’d)
Male Lock Component
Spur Gear
Notes: spur gear measures approx. 2/3” in max diameter

## Slide 21: Summary of Body Components

## Slide 22: Manufacture

## Slide 23: Standard Parts
Ball Plunger
Flanged Nut
Springs
Straps
Rivets
Screws
Oval Sleeve
Wire Rope
1/32”
Notes: acquisition of standard parts

## Slide 24: Purchased Parts w/ Modifications
Hex Stock
Spur Gear
Racks

## Slide 25: Prototyping
Component | Cost (Dollars)
Body | 148
Cover Plate | 122
Knob | 60
Lock Ring | 110
Racks (x2) | 156
Shaft | 122
Spring Base | 136
Spring Shell | 136
Spur Gear | 25
Assembly | 3.25
Springs | 21.80
Locknut | 5.11
Ball Plunger | 4.23
TOTAL | $1050
Total Cost: $1050

## Slide 26: Mass Production
Component | Cost (Dollars)
Body | 4.10
Cover Plate | 4.10
Knob | 7
Lock Ring | 21.80
Racks (x2) | 31.50
Shaft | 4.15
Spring Base | 15.7
Spring Shell | 14
Spur Gear | 12.15
Assembly | 3.25
Springs | 21.80
Locknut | 1.02
Ball Plunger | 4.23
TOTAL | $145
Total Cost: $145
Notes: assembly done by TVR Machine

## Slide 27: Lead Times
Prototype – 4 weeks
Molds – 12 weeks
1000 Parts – 5weeks
Notes: 5 weeks from the time order placed with TVR with all necessary materials delivered at that time as well

## Slide 28: Conclusions

## Slide 29: Prospective Conclusions
Further Improvements of Design
  reduction in cost
  thinner profile
  clearer presentation of indicator system
Additional Designs
  adult size
  development and incorporation of distal strap
Intellectual Property Considerations
  possible patents for indicator system and assembly method
  undesirable increase in cost to user
Notes: desig

## Slide 30: Retrospective Conclusions
Did we solve the problem – reducing user error
Revising our Project Path
  choices made in development of AFO-FD
  allowing modification of actual manufacture process
  incorporating more features of the orthotic
Revising our Course Path
  selection of design topic
  bioengineering or biotech focus
    insufficient preparation for purely mechanical design
Semester Trends
  compromise and balance of leadership
  allowance for repeating work and addressing myriad of small details

## Slide 31: Frequently Asked Questions
What is your name? – Bryce Miller
What is your group number? – 11